Features

- Wi-Fi Compliant with IEEE 802.11g and IEEE 802.11b Standards

- High-Speed up to 300Mbps Data Rate using IEEE 802.11n (draft) connection

- Built-in 3 Fixed External Antennas (MIMO Technology) to support high speed performance and great coverage

- Supports Access Point Mode and WDS feature

- Supports 64/128-bit WEP(Hex) Encryption

- Supports WPA/WPA2 and WPA-PSK/WPA2-PSK Encryption

- Supports MAC Address Filter (up to 16 entries) and SSID Broadcast Control

- Built-in DHCP Server and Client and Time Server support

- Flash Memory for Firmware Upgrade and Easy Management via Web Browser (HTTP)

- Compliant with Windows 95/98/NT/2000/XP/2003 Server/Vista, Linux and Mac OS

- Coverage up to 150 meters (500ft.) Indoor (depends on the environment)

- Coverage up to 400 meters (1300ft.) Outdoor (depends on the environment)

- 3-Year Warranty

Specification

| Hardware |
| --- |
| Standards | Wired: IEEE 802.3 (10Base-T), IEEE 802.3u (100Base-TX) Wireless: IEEE 802.11b, IEEE 802.11g, IEEE 802.11n (draft) |
| Interface | 1 x 10/100Mbps Auto-MDIX LAN Port |
| Reset Button | Reset to Factory Default Settings |
| Slide Switch | Turn On/Off Wireless LAN |
| Config Button | Reserved for WPS function use |
| LED Indicator | Power, LAN, WLAN |
| Power Adapter | 12V DC, 1A External Power Adapter |
| Power Consumption | 6W @ 12V DC |
| Dimension (L x W x H) | 180 x 122 x 30 mm (6.8 x 4.6 x 1.1 inches) |
| Weight | 320g (0.7 lbs) |
| Temperature | Operation: 0(~ 40(C (32(F~ 104(F) Storage: -20(~ 60(C (-4(F~140 (F) |
| Humidity | Max. 90% (Non-Condensing) |
| Certification | CE, FCC |
| Wireless |
| Frequency | 2.412 ~ 2.462 GHz (FCC) 2.412 ~ 2.472 GHz (ETSI) |
| Antenna | 3 x 4dBi Fixed Dipole Antenna |
| Media Access Protocol | CSMA/CA with ACK |
| Data Rate | 802.11b: 11Mbps, 5.5Mbps, 2Mbps, and 1Mbps 802.11g: 54Mbps, 48Mbps, 36Mbps, 24Mbps, 18Mbps, 12Mbps, 9Mbps and 6Mbps 802.11n (draft): up to 300Mbps |
| Security | Encryption: Hardware AES/TKIP, 64/128-bit WEP (Hex) 802.1X/EAP: WPA/WPA2/802.1X authenticator WPA: WPA-PSK/WPA2-PSK, WPA-enterprise, WPA2-enterprise SSID Broadcast Control |
| Output Power | 802.11b: 18dBm (typical) 802.11g: 15dBm (typical) 802.11n (draft): 14dBm (typical) with HT20 & HT40 |
| Receiving Sensitivity | 802.11b: -84dBm (typical) @ 11mpbs 802.11g: -72dBm (typical) @ 54Mbps 802.11n (draft) : -70dBm (typical) with HT40 |
| Channels | 1~ 11 (US), 1~13 (EU) |

Package Contents				Related Products

- TEW-630APB				- TEW-621PC

- Multi-Language Quick Installation Guide	- TEW-623PI

- CD-ROM (User’s Guide)			- TEW-624UB

- Power Adapter (12V DC, 1A)		- TEW-631BRP

- RJ-45 Cable (1.5m)

To order please call: 888-326-6061

20675 Manhattan Place, Torrance, CA 90501 • (310) 961-5500 • Fax: (310) 961-5500

Sales: sales@trendnet.com • Support: techsupport@trendnet.com

www.TRENDnet.com

# Text boxes

### 300Mbps Wireless N Access Point

The 300Mbps Wireless N Access Point incorporates the latest wireless networking technology to supercharged speed, range and performance of your wireless network. This device utilizes three external antennae to increase wireless data coverage throughout homes and businesses. IEEE 802.11n technology allows wireless clients to connect at data rates up to 300Mbps.  This IEEE 802.11n/b/g 2.4GHz access point features WEP and WPA encryption for secured wireless data transmission. WDS technology allows users to extend the wireless network by adding an additional Wireless N Access Points.  Increased speed and throughput makes it the perfect solution to fulfill your wireless needs.

TEW-630APB (V2.0R)