Features

- Wi-Fi Compliant with IEEE 802.11n (draft) and IEEEE 802.11b/g Standards

- 4 x 10/100Mbps Auto-MDIX LAN Port and 1 x 10/100Mbps WAN Port (Internet)

- Supports Cable/DSL Modems with Dynamic IP, Static IP, PPPoE, PPTP and L2TP Connection Types

- High-Speed up to 300Mbps Data Rate using IEEE 802.11n (draft) connection

- Built-in 3 External Antennas to support high speed performance and great coverage

- Firewall features Network Address Translation (NAT), and Stateful Packet Inspection (SPI) protects against Dos attacks

- Traffic Control with Virtual Server (max 64 configurable servers), special applications, Gaming types &

Ubicom StreamEngine™ Feature

- UPnP (Universal Plug & Play) and ALGs Support for Internet applications such as Email, FTP, Gaming, Remote Desktop,

Net Meeting, Telnet, and more

- Provides Additional Security of Enable/Disable SSID, Access Control, Web & Inbound traffic filters

- Supports Multiple and Concurrent IPSec, L2TP and  PPTP VPN Pass-Through Sessions

- Flash Memory for Firmware Upgrade, Save/Restore Settings

- Easy Management via Web Browser (HTTP) and Remote Management

- Supports 64/128-bit WEP, WPA/WPA2 and WPA-PSK/WPA2-PSK

- Compliant with Windows 95/98/NT/2000/XP/2003 Server, Linux and Mac OS

- Coverage up to 150 meters (500ft.) Indoor(depends on the environment)

- Coverage up to 400 meters (1300ft.) Outdoor(depends on the environment)

- 3-Year Warranty

Specification

| Hardware |
| --- |
| Standards | Wired: IEEE 802.3 (10Base-T), IEEE 802.3u (100Base-TX) Wireless: IEEE 802.11b, IEEE 802.11g, IEEE 802.11n (draft) |
| WAN | 1 x 10/100Mbps Auto-MDIX Port (Internet) |
| LAN | 4 x 10/100Mbps Auto-MDIX Port |
| Slide Switch | Turn On/Off Wireless LAN |
| Connection Type | Dynamic IP, Static (Fixed) IP, PPPoE, PPTP, L2TP |
| NAT Firewall | 4K ~ 16K Configurable NAT entries; Restricted NAPT IP Ranges, Port Ranges & Schedule Pre-Defined Game Hosting Configurations Port Triggering for 64 Special Applications ALG Support – RTP/RTSP, AOL, FTP, ICMP, WMP/MMS, NetMeeting, SIP ALG Enable/Disable |
| SPI Firewall | UP to 64 Rules for Rule-Based Firewall Cyber Attack Protection – Verified Against Over 2000 Attacks |
| Multicast Stream | Enable/Disable control support |
| UPnP | UPnP IGD Compliant |
| DMZ | DMZ Host, 64 Configurable Virtual Servers & Game Servers |
| DNS | Static or WAN assigned DNS Servers 8 Verified Services for DDNS |
| Internet Access Control | Policy Based Parental Controls, Time Based Internet Access, Port Range/Service Filtering, URL Filtering, Inbound Filter, 20 User Defined Schedules, 20 MAC Address Filter Entries |
| LED Indicator | Power, LAN1~LAN4, WAN, WLAN |
| Power Adapter | 5V DC, 2.5A External Power Adapter |
| Power Consumption | 6W @ 5VDC |
| Dimension (L x W x H) | 180 x 122 x 30 mm (6.8 x 4.6 x 1.1 inches) |
| Weight | 350g (0.8 lb) |
| Temperature | Operation: 0(~ 40(C (32(F~ 104(F) Storage: -20(~ 60(C (-4(F~140 (F) |
| Humidity | Max. 90% (Non-Condensing) |
| Certifications | FCC & CE |
| Wireless |
| Frequency | 2.412 ~ 2.462 GHz (FCC) 2.412 ~ 2.472 GHz (ETSI) |
| Antenna | 2 x 4dBi Fixed Dipole Antenna 1 x 4dBi Detachable Dipole Antenna |
| Media Access Protocol | CSMA/CA with ACK |
| Data Rate | 802.11b: 11Mbps, 5.5Mbps, 2Mbps, and 1Mbps 802.11g: 54Mbps, 48Mbps, 36Mbps, 24Mbps, 18Mbps, 12Mbps, 9Mbps and 6Mbps 802.11n (draft): up to 300Mbps |
| Security | Encryption: Hardware AES/TKIP, 64/128-bit WEP (Hex/Passpharse) WPA: WPA/WPA2(EAP/802.1x), WPA-PSK/WPA2-PSK SSID Broadcast Control |
| Output Power | 802.11b: 18dBm (typical) 802.11g: 15dBm (typical) 802.11n (draft): 14dBm (typical) with HT20 & HT40 |
| Receiving Sensitivity | 802.11b: -84dBm (typical) @ 11mpbs 802.11g: -72dBm (typical) @ 54Mbps 802.11n (draft) : -70dBm (typical) with HT40 |
| Channels | 1~ 11 (US), 1~13 (EU) |

Package Contents					Related Products

- TEW-631BRP					- TEW-621PC

- Multi-Language Quick Installation Guide		- TEW-623PI

- CD-ROM (User’s Guide)				- TEW-630APB

- Power Adapter (5V DC, 2.5A)

- RJ-45 Cable (1.5m)

To order please call: 888-326-6061

3135 Kashiwa Street • Torrance, CA 90505 • (310) 891-1100 • Fax: (310) 891-1111

Sales: sales@trendware.com • Support: techsupport@trendware.com

www.TRENDnet.com

# Text boxes

### 300Mbps Wireless N-Draft Firewall Router

The 300Mbps Wireless N Draft Router incorporates the latest wireless networking technology to increase speed, range and reliability of your wireless network.  Advanced antenna technology increases wireless data coverage throughout homes and businesses.   Increased speed and throughput makes it the perfect solution to fulfill your multimedia needs.

TEW-631BRP (V1.0R)