TREND SPEC’S

| Frequency range: | 2400 MHz – 2500MHz |
| --- | --- |
| Gain: | 4.0 dBi |
| VSWR: | 2.0 : 1 Max. |
| Polarization: | Linear, vertical |
| HPBW / horizontal: | 360 |
| HPBW / vertical: | 40 |
| Power handling: | 20 W (cw) |
| Impedance: | 50 Ohms |
| Connector: | Reverse SMA plug (female) |
| Cable: | RG-316; 100 cm (3.3 feet) |
| Weight (appr.): | 199 grams (7 Oz.) (includes base) |
| Temperature: | -10o C ~ 55o C (14o F ~ 131o F) |
| Humidity: | 95% at 25 o C (77o F) |
| Warranty: | 3 Years |
| * This Figure does not include cable loss |

TEW-IA04O    4dBi Omni Antenna (indoor) for IEEE 802.11b 2.4GHz ISM Band

TEW-IA06D    6dBi Directional Antenna (indoor) for IEEE 802.11b 2.4 GHz ISM Band

TEW-OA14D   14dBi Directional Antenna (outdoor) for IEEE 802.11b 2.4 GHz ISM Band

To order please call: 888-326-6061

3135 Kashiwa Street • Torrance, CA 90505 • (310) 891-1100 • Fax: (310) 891-1111

sales@trendware.com • techsupport@trendware.com

# Text boxes

Mounting Configuration

PRODUCT

INFORMATION

TEW-IA04O

Pattern

## 4 dBi Omni Indoor Antenna

TRENDnet’s TEW-IA04O Omni Antenna provides more power and farther distance range for your wireless network.   As an optional antenna for your IEEE 802.11b 2.4GHz 11Mbps wireless network equipments, it improves signal strength/signal quality and increases the coverage area. Designed for TEW-203PI, TEW-210APB, TEW-211BRP and TEW-303PI, you can simply place the antenna on level surface or secure it on the wall. Unleash the power of your wireless products with TRENDnet’s TEW-IA04O antenna.  Will work with any brand with Reverse SMA Male Connector!

Dimensions