#### Features

- Compliant with IEEE 802.3ab 1000Base-T, IEEE 802.3z 1000Base-SX Gigabit Ethernet Standards

- Provides One 1000Base-T Port, one 1000Base-SX Port

- Support Full-Duplex and Auto-Negotiation Mode for Fiber Port

- Provide Dip Switch to settings: Fiber (Auto/Manual), LLR (Enable/Disable)

- Hot Pluggable & Wall-Mountable

- Optional 19” System Chassis (TFC-1600) holds up to 16 Media Converters

- 5-Year Warranty

Management Features

- Support LLCF (Link Loss Carry Forward, Link Pass Through)

- Support LLR (Link Loss Return) for FX Port

- Monitor the Status of Duplex/Link with TFC-1600 and TFC-1600MM

- Set Duplex force, LLCF on/off, LLR on/off for FX, ports on/off with TFC-1600 and TFC-1600MM

- Provides Link Down Source Port Information

#### Specifications

| Hardware |
| --- |
| Standard | IEEE 802.3ab 100Base-T ; IEEE 802.3z 1000Base-SX |
| Network Media | 1000Base-TX: UTP Cat. 5, 5E, 6 EIA/TIA-568 100-ohm STP 1000Base-SX: 50/125μm Multi-Mode Fiber Optic Cable, Up to 550m 62.5/125μm Multi-Mode Fiber Optic Cable, Up to 220m |
| Protocol | CSMA/CD |
| Ports | 1 x 1000Base-T with RJ45 Connector 1 x 1000Base-SX with SC connector |
| Transfer Rate | 1000Mbps (Full Duplex) |
| DIP Switch | Auto Negotiation or Manual for FX LLR Enable or Disable for FX |
| Diagnostic LED | Power, Link/Activity |
| Power Adapter | 7.5V DC, 1.5A External Power Adapter |
| Power Consumption | 6.0 watts (max) |
| Dimensions | 120 x 88 x 25mm (4.7 x 3.46 x 0.98 inches) |
| Weight | 354g (12.5oz) |
| Temperature | Operating : 0( ~ 40( C (32( ~ 104( F); Storage : -25( ~ 70( C (-13( ~ 158( F) |
| Humidity | 5% ~ 90% RH |
| Certification | FCC,CE |

To order please call: 888-326-6061

3135 Kashiwa Street • Torrance, CA 90505 • (310) 891-1100 • Fax: (310) 891-1111

## Sales: sales@trendware.com  • Support: techsupport@trendware.com

Official Site: www.TRENDnet.com

# Text boxes

1000Mbps TX to 1000Base-FX Fiber Converter

TRENDnet’s TFC-1000 series Fiber Media Converter transforms 1000Base-T (Copper Gigabit) media to 1000Base-SX/LX (Fiber Gigabit) media and vice versa. The 1000Base-T port supports full-duplex Gigabit connection at wire speed with RJ45 connector. The fiber Gigabit connection supports shortwave (SX) or longwave (LX) laser optic with multi-mode or single-mode SC type connector. This converter will give your Copper Gigabit connection the ability to interface with fiber connection over a distance up to 40 Km. With the optional 16-slot EIA-19” rack-mount chassis, the TFC series converters are the perfect solutions for various fiber media conversions for your network.

TFC-1000MSC (b1)