#### Features

- Compliant with IEEE 802.3 10Base-T and IEEE 802.3u 100Base-TX, 100Base-FX Standards

- Provides Dip switch to set: Fiber (FDX/HDX), UTP (Auto Negotiation/Manual), Speed (10M/100M), LLR (Enable/Disable), LLCF (Enable/Disable)

- Support LLCF (Link Loss Carry Forward, Link Pass Through)

- Support LLR (link Loss Return) for FX port

- Monitor the status of duplex/link for FC, duplex / speed / link for TX via management module (TFC-1600MM) through Media Converter Chassis System (TFC-1600)

- Hot Pluggable & Wall-Mountable

- Optional 19” System Chassis (TFC-1600) holds up to 16 Media Converters

- 5-Year Warranty

#### Specifications

| Model Name | Media | Wavelength | Pout (dBm) | Sensitivity | Power | Distance |
| --- | --- | --- | --- | --- | --- | --- |
| TFC-110S15i | SMF | 1310nm | -20 ~ 0 | -32dB | 12dB | 15km |
| TFC-110S30i | SMF | 1310nm | -15 ~ -8 | -34dB | 19dB | 30km |
| TFC-110S60i | SMF | 1310nm | -5 ~ 0 | -35dB | 20dB | 60km |

| Hardware |
| --- |
| Standard | IEEE 802.3 10Base-T IEEE 802.3u 100Base-TX, 100Base-FX |
| Network Media | 10Base-T: UTP Cat. 3, 4, 5, EIA/TIA-568 100-ohm STP 100Base-TX: UTP Cat. 5, EIA/TIA-568 100-ohm STP 100Base-FX: 9/125μm or 10/125μm Single-Fiber Optic Cable, up to 60km |
| Protocol | CSMA/CD |
| Ports | 1 x 10/100Base-TX RJ-45 Port 1 x 100Base-FX Single-Mode Fiber Port SC Connector |
| Dip Switch | Duplex mode for TX/FX, Auto Negotiation or Manual for TX, Speed (10M/100M) for TX, LLR (enable/disable) for FX, LLCF (enable/disable) |
| Transfer Rate | 100Base-TX : 200Mbps (Full Duplex) |
| Diagnostic LED | Per unit: Power Per port (TX): Link/Activity, FDX/HDX, Link Fail, Speed (FX): Link/Activity, FDX/HDX, Link Fail |
| Power Adapter | 7.5V DC, 1.5A External Power Adapter |
| Power Consumption | 7.2 watts (max) |
| Dimensions | 120 x 88 x 25mm (4.7 x 3.46 x 0.98 inches) |
| Weight | 354g (12.5oz) |
| Temperature | Operating : 0( ~ 40( C (32( ~ 104( F) Storage : -25( ~ 70( C (-13( ~ 158( F) |
| Humidity | 5% ~ 90% RH |
| Certification | FCC,CE |

To order please call: 888-326-6061

20675 Manhanttan Place • Torrance, CA 90501 • (310) 961-5500 • Fax: (310) 961-5511

Sales: sales@trendnet.com • Support: support@trendnet.com

Tech Support Hotline: (888)777-1550

www.trendnet.com

# Text boxes

TFC-110S15i/30i/60i (A1.0R)

_

Intelligent 10/100Base-TX to 100Base-FX Fiber Converter

TFC-110Sxxs series Fiber Converter transforms 10/100Base-TX UTP/STP media to 100Base-FX media and vice versa. The 10/100Base-TX port auto-sense 10 or 100Mbps connection speeds, auto-negotiates half-/full-duplex mode, and auto-MDIX media type. This converter gives your switch the ability to interface with fiber connection over a distance up to 60 Km.