#### Features

- Compliant with IEEE 802.3 10Base-T and IEEE 802.3u 100Base-TX, 100Base-FX Standards

- Provides Dip Switch for Fiber(FDX/HDX), UTP (Auto Negotiation/Manual), Speed(10/100M), LLR (Enable/Disable), LLCF (Enable/Disable)

- Support LLCF (Link Loss Carry Forward, Link Pass Through)

- Supports LLR (Link Loss Return) for FX Port

- Single-Strand Fiber Optic, Hot Pluggable & Wall-Mountable

- Optional 19” System Chassis (TFC-1600) holds up to 16 Media Converters

- 5-Year Warranty

#### Specifications (MMF: Multi-Mode Fiber)

| Model Name | Wavelength | Pout | Sensitivity | Power |
| --- | --- | --- | --- | --- |
| TFC-110S20D3 | TX: 1310nm; RX: 1550nm | -15dBm | -32dB | 17dBm |
| TFC-110S20D5 | TX: 1550nm; RX: 1310nm | -18dBm | -32dB | 14dBm |

| Hardware |
| --- |
| Standard | IEEE 802.3 10Base-T IEEE 802.3u 100Base-TX, 100Base-FX |
| Network Media | 10Base-T: UTP Cat. 3, 4, 5, EIA/TIA-568 100-ohm STP 100Base-TX: UTP Cat. 5, EIA/TIA-568 100-ohm STP 100Base-FX: 9/125μm or 10/125μm Single-Fiber Optic Cable, up to 20km |
| Protocol | CSMA/CD |
| Ports | 1 x 10/100Base-TX RJ-45 Port 1 x 100Base-FX Single-Fiber Bi-Directional Port SC Connector |
| Dip Switch | TX: Duplex Mode, Auto Negotiation or Manual, Speed, LLCF (enable/disable) FX: Duplex Mode, LLR (enable/disable), LLCF |
| Transfer Rate | 10Base-T : 10Mbps/20Mbps (Half/Full Duplex) 100Base-TX : 100Mbps/200Mbps (Half/Full Duplex) |
| Diagnostic LED | Per Unit : Power Per Port : Link/Activity, FDX/HDX, Link Fail, Speed (only for TX Port) |
| Power Adapter | 7.5V DC, 1.5A External Power Adapter |
| Power Consumption | 7.2 watts (max) |
| Dimensions | 120 x 88 x 25mm (4.7 x 3.46 x 0.98 inches) |
| Weight | 354g (12.5oz) |
| Temperature | Operating : 0( ~ 40( C (32( ~ 104( F) Storage : -25( ~ 70( C (-13( ~ 158( F) |
| Humidity | 5% ~ 90% RH |
| Safty Emissions | FCC,CE |

To order please call: 888-326-6061

3135 Kashiwa Street • Torrance, CA 90505 • (310) 891-1100 • Fax: (310) 891-1111

Sales: sales@trendnet.com • Support: techsupport@trendnet.com

Tech Support Hotline: (888)777-1550

www.trendnet.com

# Text boxes

10/100Mbps TX to 100Base-FX Dual-Wavelength

Single-Mode Fiber Converter

The Single-strand fiber products use optics that transmit and receive on two different wavelengths; you must deploy single-strand fiber products in pairs, or connect two compatible TFC-110S20 series single-strand fiber products. For example, connect TFC-110S20D3 (which has 1310 transmit and 1550 receive) to TFC-110S20D5 (which has 1550 transmit and 1310 receive). The two connected products must also have the same speed, and distance capabilities (i.e. both support single-mode, 20km distance).

TFC-110S20D3/D5