Features

- Compliant with USB 2.0 and USB 1.1 Specifications

- Compliant with V.92, V.90, V.44 Standards

- Supports V.44 and V.92 Quick Connect, PCM Upstream and Modem On Hold Features

- Up to 56Kbps Data Download Speed and 48Kbps Data Upload Speed

- Hosts Signal Processing for both controller and data -pump

- Voice/Telephone Answering Machine support via Sound Card

- Video Phone ready (Interface to H.324 Video Conferencing Support)

- Compatible with Windows 98SE/ME/2000/XP/2003 Server

- Support ITU-T T.31 Class 1 fax with transfer rate up to 14.4kbps.

- USB Bus-Powered method and Low Power consumption

- Includes Data/Fax/Voice Communication Software

- LED Display

- 3-Year Warranty

Specifications

| Hardware |
| --- |
| Standard | USB 2.0 USB 1.1 |
| Interface | 1 x USB 2.0 /1.1 (Type A) 1 x RJ-11 Port (Phone Line) |
| Data Mode | V.92 & V.90, V.34, V.32(bis), V.22(bis), V.22, V.23, V.21, Bell 212A, Bell 103 |
| Error Correction | V.42, LAPM & MNP 2-4 |
| Data Compression | V.44, V.42(bis) & MNP5 |
| Fax Mode | ITU-T V.17, V.29, V.27ter and V.21 ch2, ITU-T T.31 Class1 Fax |
| Power Management | USB Bus-Powered |
| Power Consumption (Input 3.3VDC) | Idle Mode: 65mW Operating Mode: 134mW |
| Dimensions | 100 x 35 x 23mm (3.94 x 1.38 x 0.91in.) |
| Weight | 25g (0.88oz.) |
| Temperature | Operating: 0°C~ 40°C (32°F~ 104°F) Storage: -20°C~ 60°C (-4°F~140°F) |
| Humidity | 10%~90% (non-condensing) |
| Certifications | FCC, CE |
| Functions |  |
| Supported OS | Windows 98SE/ME/2000/XP/2003 Server |
| Voice Function | - TAM (USA) Support with Concurrent DTMF Detect, Ring Detect - 8-Bit u– Law/A-Law (G711) Coding - 8000 Hz Sample Rate |
| Video Phone Ready | - V.80 sync Access mode Supports Host-Controlled Communication Protocol - H.324 interface Support |
| Multiple Country | Call Progress, Blacklisting Support |
| Miscellaneous | - Data/Fax/Voice Call Discrimination - Single Profile Stored in Host - Modem and audio paths - DTMF |

## Package Content							Related Product

- TFM-560U								- TFM-PCIV92A

- Multi-Language Quick Installation Guide				- TFM-560X

- Driver CD-ROM

- RJ-11 Telephone Cable

To order please call: 888-326-6061; Sales: sales@trendnet.com

Support: support@trendnet.com; Tech Support Hotline: 310-626-6252

Official Site: www.trendnet.com

# Text boxes

TFM-560U

### 56K (V.92) High Speed USB 2.0 Fax/Data/Voice Modem

56K (V.92) High Speed USB 2.0

Data/Fax/Voice Modem

The TFM-560U High Speed USB 2.0 Fax Modem delivers fast access to the Internet with more efficient upload and download speeds. The V.92/V.44 standard modem offers the highest possible data transfer rates and reliable fax transmissions.  The modem utilizes the latest V.92 standard providing Internet connection features such as Quick Connect, Modem-on-Hold, and 48Kbps upload rates.

TFM-560U (Version B1)

Modem Solution for TFM-560U

Interface