Features

- 3 x IEEE 1394 FireWire Port

- 32-bit 33Mhz host interface compliant to PCI Specification 2.2

- Supports PCI-Bus Power Management Interface Specification 1.1

- Compliant with IEEE1394A Standard and Backward Compatible with IEEE 1394-1395 Devices

- Provides High Speed Data Transfer Rate up to 400Mbps

- Provides Software Interrupt Control

- Supports up to 63 FireWire Devices

- Supports Windows 98SE/ME/2000/XP and Mac OS 8.6 or Above

- Supports Plug & Play and Easy Installation

- 2-Year Warranty

Specifications				   Solution for TFW-H3PI

| Hardware |
| --- |
| Interface | 32-bit PCI rev. 2.2 |
| Standards | IEEE 1394A, 1394-1395 |
| Ports (6-pin) | 3 x IEEE 1394 FireWire Ports |
| OS Compliant | Windows 98SE/ME/2000/XP Mac OS 8.6 or Above |
| Data Rate | 100/200/400Mbps |
| Power Consumption | 500mA (max) per port |
| Dimensions (LxWxD) | 134 x 121 x 21.6mm (5.3 x 4.76 x 0.85 inches) |
| Weight | 66g (0.15lb) |
| Operating Temperature | 0( ~ 40( C (32( ~ 104( F) |
| Storage Temperature | -10( ~ 45( C (14( ~ 113( F) |
| Humidity | 0 %~ 85% (Non-Condensing) |
| Certification | FCC, CE |

Package Contents			System Requirement

- TFW-H3PI				-    System with Supported Operating System

- Quick Installation Guide		-    64MB RAM or More

- 1 x FireWire Cable (6ft.)		-    Available PCI Version 2.2 Slot

-    CD-ROM Drive for Driver Installation

# Text boxes

TFW-H3PI

3-Port FireWire Host PCI Adapter

This 3-Port FireWire Host PCI Adapter gives your Desktop PC three IEEE 1394 FireWire ports so you can easily connect to digital camcorders, external hard-drives, and other FireWire peripherals.

TFW-H3PI (v1.1R)