Features

- Use one keyboard, monitor, and mouse to control two computers

- USB Keyboard/Mouse emulation with 2-set of detachable KVM Cables

- Supports Microsoft Intellimouse, Optical Mouse, Logitech Net Mouse and more

- Supports super High Video Quality, up to 2048 x 1536 VGA resolution

- Supports Windows 98/98SE/ME/2000/XP/2003 Server, Linux, and Mac OS

- Multi-Platform support for PCs, Macintosh G3/G4, iMac and Mac Mini

- Hot-Plug pluggable.  Adds PC or removes the connected PCs for maintenance without powering down the KVM Switch or other PC’s.

- Switches PC by hot-keys, push button or windows-base client switch software.

- Auto-Scan & LED display for easy status monitoring

- User definable hot-key (Windows Only)

- USB Interface Power method

- 2-Year Warranty

Specifications

| Hardware |
| --- |
| Computer Connections | 2 |
| USB Interface | USB 1.1 Specifications Compliant |
| KVM Cable | 2 Sets of 1.2M (4ft) KVM Cables |
| Cable Interface | To Console: 1 x VGA/SVGA HDB 15-pin (male) | To PC: 1 x USB (Type A) 1 x VGA/SVGA HDB 15-Pin (male) |
| Console Connectors | 2 x USB Keyboard/Mouse: (Type A) 1 x VGA/SVGA 15-pin HDB |
| Port Selection | Push Button, Hot-Key Commands or Windows-Based Client Switching Software |
| Auto-Scan Interval | 10 seconds |
| Keyboard State | Saved and Restored |
| Power Type | USB Interface Power |
| Dimensions | 98 x 70 x 28 mm (3.86 x 2.76 x 1.1 in.) |
| Weight | 99 g (3.4 oz) |
| Temperature | Operating: 0(C ~ 40(C (32(F ~104(F) Storage: -20(C ~ 60(C (-4(F ~140(F) |
| Humidity | 0%~90%, Non-Condensing |
| Certifications | CE, FCC |

Package Contents							Related Products

- TK-207								- TK-205K

- Multi-Language User’s Guide				                          - TK-208K

- Utility CD-ROM							- TK-210K
- 2 sets of USB KVM Cables

To order please call: 888-326-6061 •  Sales: sales@trendnet.com

## Support: support@trendnet.com  • Tech Support: 866-845-3673

Official Site: www.trendnet.com

# Text boxes

# 2-Port USB KVM Switch

The 2-Port USB KVM Switch lets you manage two PC’s with just one set of keyboard, monitor, and mouse. Switch between two PC’s with a simple press of a button! Separate sets of KVM cables are included with the KVM Switch, so users can start controlling 2 PC’s instantly. The KVM cables also provide power to the KVM Switch, eliminating the need for a power adapter. Hot Key operations provide immediate access to features such as computer switching, and auto-scanning.  With its Hot-Plug, and Audible Feedback, the 2-Port USB KVM Switch is the perfect choice for managing multiple PC’s.

#### TK-207K (v1.1R)

KVM Solution for TK-207K

KVM Interface