Features

- 8-Port stackable KVM Switch

- Supports Microsoft Intellimouse, Microsoft Intellimouse Explorer, Logitech NetMouse, Optical Mouse and more

- Compliant with DOS, Windows 3.x/95/98/ME/2000/XP/2003 Server, Netware, Unix, Linux, and more

- High video quality – up to 1920 x 1440 resolution

- Supports password protection

- Stackable up to 16 KVM switches (128 PCs)

- Auto-Scan for monitored PCs with adjustable scan interval from 5-99 seconds.

- Keyboard status restored when switching between PCs

- LED Display for easy status monitoring

- On Screen Display (OSD) control for easy management

- Beeping sound for port switching confirmation (enabled/disabled)

- Auto-detect bank number (when daisy-chaining)

- Built-in daisy-chain port

- Hot-key or push button switching

- Plug & Play and Hot-Pluggable

- Standard 19” (1U) rack mount design

- 2-Year Warranty

Specifications

| Hardware |
| --- |
| Management | 8 Computers |
| PC Port (all female) | 8 x PS/2 Mouse 6-pin Mini Din 8 x PS/2 Keyboard 6-pin Mini Din 8 x VGA HDB 15-pin |
| Console Port (all female) | 1 x PS/2 Mouse 6-pin Mini Din 1 x PS/2 Keyboard 6-pin Mini Din 1 x VGA HDB 15-pin |
| Daisy Chain Port (all female) | 1 x PS/2 Mouse 6-pin Mini Din 1 x PS/2 Keyboard 6-pin Mini Din 1 x VGA HDB 15-pin |
| Cable | 1 x Daisy-Chain Cable (male to male) |
| Supported OS | DOS, Windows 3.x/95/98/ME/2000/XP/2003 Server Linux, Unix and more |
| PC Selection | On Screen Display (OSD) Control, Hot-Key or Push Button |
| Daisy Chain Level | Up to 16 KVM Switches (128 PCs) |
| Auto-Scan Interval | 5-100 seconds (Programmable through Hot-Key) |
| LED | Unit: Bank (Red) Port: Link (Red) and Select (Green) |
| Keyboard Status | Saved & Restored |
| Power Adapter | 9V DC 1A External Power Adapter |
| Dimensions | 407 x 165 x 45mm (16 x 6.5 x 1.8in.) |
| Weight | 1.97 kg (4.33lb) |
| Temperature | Operating: 0(C~40(C (32(F~104(F) Storage: -20(C~60(C (-4(F~140(F) |
| Humidity | 0%~80% (non-condensing) |
| Certification | CE, FCC |

Package Contents							Related Products

- TK-802R								- TK-802R

- Multi-Language Quick Installation Guide				- TK-803R

- Daisy Chain Cable							- TK-1602R

- Power Adapter (9V DC, 1A)

- Rack Mount Kit

To order please call: 888-326-6061; Sales: sales@trendnet.com

Support: support@trendnet.com; Tech Support Hotline: 866-845-3673

Official Site: www.trendnet.com

# Text boxes

8-Port Stackable Rack Mount KVM Switch with OSD

TK-802R 8-port Stackable KVM Switch allows you to manage multiple PCs with just one keyboard, monitor and mouse. Switching between PCs with a simple press of a button! Eliminate the hassle of cable swapping and save money and space with TK-802R. Designed with ease of expansion in mind, you can stack up to 8 units together to control maximum of 128 PCs. With it’s rack mount size and slim one unit height, it is perfect for mounting on EIA-19” rack in the Server Room and computer lab. Rich in features such as On Screen Display (OSD) Menu, Hot-Plug, Auto-Scan, and Hot-Key operations, TK-802R is the perfect choice for managing multiple PCs.

TK-802R (Version V1.2R)

New Implements

- New Housing