FEATURES

- Support Microsoft Intellimouse, Microsoft Intellimouse Explorer, Logitech NetMouse, Optical Mouse, Cordless Mouse and other MS compatible Mouse.

- PS/2 Keyboard/Mouse emulation

- Support DOS, Windows 3.x/95/98/ME/NT/2000/XP, Netware, Unix, Linux, and more

- Very high video quality – up to 1920 x 1440 resolution and 200MHz bandwidth

- No software required – easy PC selection via Push Buttons and Hot-Key Operation

- Hot-Plug feature – add or remove PC without powering off the KVM Switch or other PCs

- Auto-Scan Mode for monitoring PCs, with configurable scan interval from 5~99 seconds

- Keyboard status restored when switching from PC to PC

- Support 8 characters password protection

- LED Display for easy status monitoring

- On Screen Display (OSD) Menu for easy management

- Beeping sound for port switching confirmation (enabled/disabled)

- Auto-detect bank number (when daisy-chaining)

- Built-in daisy-chain port (0.85 m/2.8 ft. daisy-chain cable included)

- EIA-19” rack-mountable (hardware included)

- 1-Year Warranty

TREND SPEC’S

Computer Port:	8 ports. Keyboard and Mouse: PS/2 type female mini Din 6-pin,

Monitor (Video): female HDDB 15-pin

Daisy Chain Port:	1 port. Keyboard and Mouse: PS/2 type female mini Din 6-pin, VGA female HDDB 15-pin

Console Port:	1 port. Keyboard and Mouse: PS/2 type female mini Din 6-pin, VGA female HDDB 15-pin

KVM Cable:	1 x 0.85m (2.8 feet) high-grade KVM daisy-chain cable (male-to-male)

PC Selection:	On Screen Display Menu, Hot-Keys and Push Buttons

LEDs:	One Bank LED, Two LED indicators per port (PC Link and PC Active)

Auto-Scan Intervals:	5~99 seconds

Keyboard State:	Saved and restored

Video Bandwidth:	200MHz

Power Adapter:	9V DC, 1A External Power Adapter

Dimensions:	410 x 164 x 45 mm (16.14 x 6.45 x 1.77 inches)

Weight:	Approximately 2.06 Kg. (4.55 lbs)

Operating Temp.:	0( ~ 40( C (32( ~ 104( F)

Storage Temp.:	-20( ~ 60( C (-4( ~ 140( F)

Operating Humidity:	0 ~ 90%RH, Non-Condensing

Certifications:	FCC, CE

TOP REASONS THE TK-802R IS A LASTING TREND

Integration Friendly:	Does not require driver/software for the installation and operation. Switching between PCs with the On Screen Display Menu, Push Buttons and Hot-Key operation.

Flexible:	Hot-Plug feature – add PCs or remove connected PCs without powering off the KVM Switch or the other PCs.

Cost Effective:	Manage multiple PCs with single keyboard, monitor, and mouse. Save on equipment cost, utility, and space.

Performance:	Support very High Video Quality up to 1920 x 1440 with 200MHz bandwidth. Keyboard status is saved for each PC.

TK-802R		8-Port Stackable Rack-Mount KVM Switch (with OSD)

TK-801R		8-Port KVM Rack-Mountable Switch

TK-200K		2-Port KVM Switch Kit

TK-400K		4-Port KVM Switch Kit

TK-401R		4-Port KVM Rack-Mountable Switch

TK-C06		1.8 Meters (6 Feet) KVM Cable (male-to-male)

TK-C10		3 Meters (10 Feet) KVM Cable (male-to-male)

#### To order please call: 888-326-6061

3135 Kashiwa Street • Torrance, CA 90505 • (310) 891-1100 • Fax: (310) 891-1111

##### Sales: sales@trendware.com • Support: techsupport@trendware.com	ss05302003

# Text boxes

8-Port Stackable Rack Mount KVM Switch with OSD

TRENDnet’s TK-802R 8-port Stackable KVM Switch allows you to manage multiple PCs with just one keyboard, monitor and mouse. Switching between PCs with a simple press of a button! Eliminate the hassle of cable swapping and save money and space with TRENDnet’s TK-802R. Designed with ease of expansion in mind, you can stack up to 16 units together to control maximum of 128 PCs. With it’s rack-mount size and slim one unit height, it is perfect for mounting on EIA-19” rack in the Server Room and computer lab. Rich in features such as On Screen Display (OSD) Menu, Hot-Plug, Auto-Scan, and Hot-Key operation, TRENDnet’s TK-802R is the perfect choice for managing multiple PCs.

TK-802R

KVM Solution for TK-802R

Product Information