Features

- Compliant with Hi-Speed USB 2.0 & USB 1.1 Standards

- Reads and Writes Compact Flash Type I/II Card and Micro Drive (MD) for CF/MD slot

- Reads and Writes Smart Media Card for SM slot

- Reads and Writes Memory Stick (MS), MS Duo*, MS PRO, and MS Pro Duo* for MS slot

- Reads and Writes Secure Digital (SD), Mini SD*, MultiMedia Card (MMC), and RSMMC* for SD/MMC slot

* Requires Additional Converter Adapter

- Reads/writes up to 4 different types of memory cards at the same time

- Compatible with Windows 98(SE)/ME/2000/XP, Mac OS 8.6/9/X

- Supports USB High-Speed (480Mbps), Full-Speed (12Mbps) and Low-Speed (1.5Mbps) Transfer Rates

- Supports Plug & Play and Hot-Swap

- Portable Compact Design and No External Power Source Required

- Low Power consumption (power saving mode supported)

- USB Cable Embedded on the device (75mm/3 inches). An extension cable is included.

- 2-Year Warranty

Specifications

| Interface | USB 2.0, USB 1.1 |  |  |
| --- | --- | --- | --- |
| Card Supported | CF: 8MB and up MD: 340MB and up SM: 8MB and up MS Series: 8MB and up SD: 16MB and up MMC/RSMMC: 8MB and up | Power Consumption (500mA max. per port) | No card installed: 109mA CF: 119mA (reads) 125mA (writes) MD: 149mA (reads) 390mA (writes) SM: 115mA (reads) 115mA (writes) MS Series: 116mA (reads) 119mA (writes) SD: 130mA (reads) 140mA (writes) MMC/RSMMC: 130mA (reads) 140mA (writes) |
| Sockets | CF socket x 1 for Compact Flash Type I/II Card & IBM Micro Drive; complies with CF spec 1.4 SM socket x 1 for Smart Media Card; complies with SM spec 1.1 (3.3v) MS socket x 1 for Memory Stick; complies with MS spec 1.3, MS Duo, MS PRO SD socket x 1 for Secure Digital Card & Multi-Media Card; complies with SD spec 1.0 |
| Performance (avg.) (USB1.1) | CF: Reads 1 Mbps; Writes 890 Kbps SM: Reads 973 Kbps; Writes 488 Kbps MS: Reads 632 Kbps; Writes 471 Kbps SD: Reads 194 Kbps; Writes 246 Kbps MMC: Reads 176 Kbps; Writes 219 Kbps | Performance (avg.) (USB2.0) | CF: Reads 5.4 Mbps; Writes 3.0 Mbps SM: Reads 5.0 Mbps; Writes 742 Kbps MS: Reads 858 Kbps; Writes 659 Kbps SD: Reads 7.1 Mbps; Writes 2.6 Mbps MMC: Reads 1.5 Mbps; Writes 471 Kbps |
| LED | MS, MMC/SD, CF, SM | Cable Gauge | 28/22 AWG |
| Dimensions | 110x74x14mm (4.3x 2.9 x 0.5 inch) | Weight | 85g. (3 oz.) |
| Operating Temp | 0( ~ 65( C (32( ~ 146( F) | Storage Temp | -20( ~ 80( C (-4( ~ 176 ( F) |
| Humidity | 90%RH (Non-condensing) | Certification | FCC, CE |

TOP REASONS THE TMR-61U2 IS A LASTING TREND

Integration Friendly:	Supports Windows and Mac OS

Efficiency:	Save time from retrieving data from different types of memory card devices

Flexible: 	Minimize space and cables needed for connecting various memory card readers

Cost Effective:	Reads and writes most types of memory cards (up to 4 at the same time).

Performance:		Transfer rate up to 480Mbps

Related Products					Package Contents

- TMR-41PC						- TMR-61U2

- TU2-ET200						- Driver CD-ROM

- Quick Installation Guide

- USB A-B Cable (95cm/3ft)

# To order please call: 888-326-6061

3135 Kashiwa Street • Torrance, CA 90505 • (310) 891-1100 • Fax: (310) 891-1111

## Sales: sales@trendware.com • Support: techsupport@trendware.com

Official Site: www.TRENDnet.com

# Text boxes

TMR-61U2

USB 2.0 All-in-1 Memory Card Reader/Writer

TRENDnet's TMR-61U2 USB 2.0 All-in-1 Memory Card Reader/Writer provides an ideal solution to read and write up to 6 types of memory cards including MultiMedia Card, CompactFlash Card, IBM Micro Drive, Smart Media Card, Secure Digital Card, and Memory Stick.  Its 4-slot design accommodates up to 4 different types of memory cards at the same time for convenient file transfers between different types of cards. Transfer large files between your computer, digital camera, PDA, MP3 player and more.  The TMR-61U2 has a UBS 2.0 interface that offers plug-and-play installation, Hi-Speed data transfer rate, and backward compatibility with USB1.1 interface. TRENDnet's TMR-61U2 All-in-1 Memory Card Reader/Writer provides incredibly easy and fast data transfer method for your memory cards.

TMR-61U2 USB 2.0 All-in-1 Memory Card Reader/Writer