Features

- IEEE 802.3af Power over Ethernet (PoE) Standard Compliant

- Support up to 11W at 5V DC or 12W at 12V DC

- Converts Non-PoE devices with Power Over Ethernet Support

- Advanced Auto-Sensing Algorithm enables the ability to draw power from 802.3af PSE

(Power Source Equipment) Devices

- High Safety Standards with Short Circuit Protection

- Supports Power Detection and Classification

- Auto Disconnection for Over Voltage or Under Voltage Situation

- 5-Year Warranty

Specifications

| Hardware |
| --- |
| Standard | IEEE 802.3 10Base-T IEEE802.3u 100Base-TX IEEE 802.3af Power over Ethernet |
| Network Media | 10Mbps: Cat 3,4,5 Unshielded/Shielded/Screened Cable 100Mbps: Cat 5, 5E, 6 Unshielded/Shielded/Screened Cable |
| Protocol | CSMA/CD |
| Topology | Star |
| Ports | 1 x PoE-IN Port (Data + Power) 1 x Data-OUT Port (Data only) |
| Switch | Switch between 5V and 12V |
| Power | DC Output 5V/2.2A or 12V/1A |
| Jumper Cable | 2.5mm / 0.1” Diameter on the Connector (Center Positive) |
| Diagnostic LEDs | Power In: 48V (Green) Power Out: 5V (Green) / 12V (Amber) |
| Power Consumption | 15.4 watts (max) |
| Temperature | Operation: 0(C~40(C (32(F~ (F) Storage: -10(C~70(C ((F~ (F) |
| Humidity | 10%- 90% (non-condensing) |
| Dimensions | 87 x 85 x 24mm (3.425 x 3.35 x 0.95 inches) (L x W x H) |
| Weight | 156g (0.35 lb) |
| Certification | FCC, CE |
| Image |  |

Power over Ethernet Solutions

Package Contents	Related Product

- TPE-102S						- TPE-101I

- Multi-Language User’s Guide	- TPE-S88

- Power Jumper Cable

- Cat.5 Cable (60cm/23.6inches)

To order please call: 888-326-6061

3135 Kashiwa Street • Torrance, CA 90505 • (310) 891-1100 • Fax: (310) 891-1111

### Sales: sales@trendware.com • Support: techsupport@trendware.com

Tech Support Hot Line: 1-310-626-6252

### Official Site: www.TRENDNET.com

# Text boxes

Power over Ethernet (PoE) Splitter

TRENDnet’s TPE-102S Power over Ethernet Splitter provides an innovative and cost effective solution to a variety of Ethernet devices such as VoIP phones or Wireless Access Points. Reduce costs by using existing CAT5 cable to deliver both power and data where power source is difficult to obtain.

TPE-102S (version B1)