Features

- IEEE 802.3af Power over Ethernet (PoE) Standard Compliant

- 24 x 10/100Mbps Auto-Negotiation and Auto-MDIX Fast Ethernet PoE RJ-54 Ports

- 2 x 10/100/1000Mbps Auto-Negotiating and Auto-MDIX Gigabit Ports

- Supports PoE Power up to 15.4 watts for each PoE port

- Supports PoE Power maximum up to 170 watts for all PoE ports

- Supports PoE Powered Device(PD) classification identify

- Full Wire-Speed Non-Blocking Reception and Transmission

- Store and Forward Switching Method

- 768K bytes RAM Data Buffer and 4K entries MAC Address Table

- Extensive Diagnostic LED’s on the Front Panel

- IEEE 802.3x Flow Control for Full-Duplex Mode; Back Pressure Flow Control for Half-Duplex Mode

- Proprietary Windows Based Management/Monitoring Utility (similar to SNMP Trap)

- Supports Port-Based VLAN, Trunking and Port Mirroring

- Port Setting Function, Users can set each Port’s Availability, Speed, Duplex Mode, and Flow Control

- Easy configuration via Web browser

- Standard 19” (1U) Rack-Mount size (kit included)

- 5-Year Warranty

Specifications

| Hardware |
| --- |
| Standard | IEEE 802.3 10Base-T IEEE802.3u 100Base-TX IEEE 802.3ab 1000base-T IEEE 802.3af Power over Ethernet |
| Network Media | 10BASET: 2-pair UTP Cat. 3, 4, 5; up to 100m 100BASE-TX: 2-pair UTP Cat. 5, 5E; up to 100m 1000BASE-T: 4-pair UTP Cat. 5, 5E, 6; up to 100m PoE: 4-pair UTP Cat. 5; up to 100m |
| Protocol / Topology | CSMA/CD ; Star |
| Ports | 24 x 10/100Mbps Auto-MDIX PoE Ports 2 x 10/100/1000Mbps Auto-MDIX Gigabit Ports |
| Data Transfer Rate | Ethernet: 10/20Mbps (half/full duplex) Fast Ethernet: 100/200Mbps (half/full duplex) Gigabit: 2000Mbps (full duplex) |
| RAM Buffer / Filtering | 768 K Bytes / 4K entry per device |
| Power | 100~240VAC 50/60Hz, Internal Universal Switching Power Supply |
| Diagnostic LEDs | Per Unit: Power, System Per Port: Link/Activity, Speed PoE: PoE status (bi-color LED) |
| Power Consumption (max 180 watts) | 9 watts max (no PD Device connected) 170 watts max (11 x 15.4 watts PoE Device connected) |
| Temperature | Operating: 0( ~ 40( C (32( ~ 104(F); Storage: -10( ~ 70( C (14( ~ 158(F) |
| Humidity | 10%- 90% (non-condensing) |
| Dimensions | 440 x 310 x 44 mm (17.3 x 12 x 1.73 inch) (W x H x D) |
| Weight | 4.43kg (9.75 lbs) |
| Certification | FCC, CE |
| PoE |
| Power over Ethernet | Up to 15.4 watts per Port; Max 170W for all PoE ports PD classification Identify; Manual setting for PoE power limitation Supports PoE priority setting; PoE over current protection PoE circuit sorting protection PoE power on RJ-45 pin 3,6 for Power+ and pin 1,2 for Power- |

Power over Ethernet Solutions

Package Contents	Related Product

- TPE-224WS						- TPE-101I

- Multi-Language User’s Guide	- TPE-102S

- Web-Smart Utility CD-ROM				- TPE-S88

- Power Supply

- Rack Mount Kit

To order please call: 888-326-6061

3135 Kashiwa Street • Torrance, CA 90505 • (310) 891-1100 • Fax: (310) 891-1111

### Sales: sales@trendware.com • Support: techsupport@trendware.com

Tech Support Hot Line: 1-310-626-6252

### Official Site: www.TRENDNET.com

# Text boxes

26-Port Gigabit Web Smart PoE Switch

TPE-224WS 26-port Smart Switch integrates Power over Ethernet (PoE) and network management features into a cost effective and scalable solution. The TPE-224WS reduces equipment cost by delivering data and power over existing network cable infrastructure. The switch offers advanced network management features such as VLAN and QoS to meet today’s secured network applications.

TPE-224WS