Features

- Wi-Fi Compliant with 802.11b/g Standards

- Up to 54Mbps High Speed over Wireless Connection

- Up to 85Mbps High-Speed Data Transfer Rate over Power Lines

- Supports Access Point Mode

- Dynamic Data Rate Scaling at 54, 48, 36, 24, 18, 12, 9 and 6Mbps for 802.11g

- Dynamic Data Rate Scaling at 11, 5.5, 2 and 1Mbps for 802.11b

- Supports ESSID Enable/Disable and MAC address Filter (60 entries) Feature to Increase Security

- Supports 64/128-bit Wired Equivalent Privacy (WEP) and WPA/WPA2 (EAP/PSK) Encryptions

- Wireless Range of 30 ~ 50 meters Indoor (depending on the environment)

- Wireless Range of 50 ~ 100 meters Outdoor (depending on the environment)

- Connect to a Network using exiting Powerlines with Wall-Plugged Design

- 3-Year Warranty

Specifications

| Hardware |  |
| --- | --- |
| Standards | IEEE 802.11b (11Mbps), IEEE 802.11g (54Mbps) HomePlug 1.0 Turbo |
| LED Indicators | Power, HomePlug, WLAN |
| Network Protocols | TCP/IP, UDP |
| Power Source | 100~240V AC, 50~60Hz |
| Dimensions (LxWxH) | 74 x 100 x 35 mm (2.9 x 4 x 1.3 inches) |
| Weight | 200g (7oz.) |
| Power Consumption | 3.8 watts(max.) |
| Temperature | Operating: 0(~ 40(C (32(F~ 104(F) Storage: -10(~ 70(C (14(F~ 158(F) |
| Certification | FCC, CE |
| Powerline |  |
| Frequency Band | 2MHz ~ 30MHz |
| Data Rate | Up to 85Mbps Transfer Rate |
| Nodes | Support up to 16 nodes per Network |
| Security | 56-bit DES Encryption |
| Wireless |  |
| Module Technique | OFDM, CCK, DQPSK, DBPSK |
| Frequency Range | 2.4 ~ 2.4835 GHz |
| Antenna | 2dBi Detachable Dipole Antenna |
| Data Rate (auto fallback) | 802.11b: 11Mbps, 5.5Mbps, 2Mbps, and 1Mbps 802.11g: 54Mbps, 48Mbps, 36Mbps, 24Mbps, 18Mbps, 12Mbps, 9Mbps and 6Mbps |
| Security | 64/128-bit WEP (HEX/ASCII), WPA/WPA-PSK (AES/TKIP), WPA2/WPA2-PSK (AES/TKIP) |
| Transmit Power | 13.5 ±1.5dBm (typical) |
| Channels | 1~11 channels (US), 1~13 channels (EU) |

Package Contents			Related Products

- TPL-210AP				- TPL-202E

- Quick Installation Guide		- TPL-101E

- Utility CD-ROM			- TPL-111BR

To order please call: 888-326-6061

20675 Manhattan Place • Torrance, CA 90501 • (310) 891-1100 • Fax: (310) 891-1111

### Sales: sales@trendnet.com • Support: techsupport@trendnet.com

Tech Support Hot Line: 1-866-845-3673

### Official Site: www.TRENDNET.com

# Text boxes

TPL-210AP (v1.0R)

85Mbps Powerline Wireless Access Point

The Wireless Powerline Access Point removes additional costs in network cabling by using existing power lines in your home or small office to network several wireless workstations.  Secure file sharing, an Internet connection, or other network resources by using 56-bit DES for 85Mbps power line transmission and WPA security for 54Mbps wireless transmission.