Features

- Compliant with USB 1.1 and 1.0 Specifications

- Compliant with IEEE 802.3 and IEEE 802.3u Specifications

- Supports both full-duplex and half-duplex operations

- Supports Self-Powered Device Configurations

- Compatible with Windows 98(SE)/ME/2000/XP Operating Systems

- Diagnostic LED

- Supports Plug & Play and Easy Installation

- 5-Year Warranty

Specifications

| Hardware |
| --- |
| Standards | USB 1.1 IEEE 802.3 10Base-T IEEE 802.3u 100Base-TX |
| Data Transfer Rate | Ethernet: 10Mbps/20Mbps (Half/Full Duplex) Fast Ethernet: 100Mbps/200Mbps (Half/Full Duplex) USB: 12Mbps |
| Supported OS | Windows 98(SE)/ME/2000/XP |
| Power | Bus-Power |
| Diagnostic LED | Link/ACT |
| Dimensions | 65 x 48 x 28mm(2.6 x 1.9 x 1.1 in.) |
| Weight | 71g. (2.5 oz.) |
| Operating Temp. | 0(C~ 40(C (32(F ~ 104(F) |
| Storage Temp. | -10(C ~ 70(C (14(F~ 158(F) |
| Humidity | 0 ~ 90% (Non-Condensing) |
| Certification | CE, FCC |

Package Contents			Related Products

- TU-ET100C				- TU-400E

- Quick Installation Guide		- TU2-ET100

- Driver CD-ROM			- TU2-H2PC

# Text boxes

TU-ET100C (Version v3.1)

USB to 10/100Mbps Fast Ethernet Adapter

TU-ET100C is a compact 10/100Mbps network adapter for the USB interface. The TU-ET100C features plug-n-play installation and it is compatible with Windows 98/ME/2000/XP. The TU-ET100C draws power directly from PCs, perfect for laptop and desktop users.

New Implement:

- New TRENDnet Logo

- Clam shell packaging