Features

- Compliant with USB 1.1 and USB 1.0 Specifications

- Converts two PS/2 devices simultaneously (keyboard and mouse) to the USB interface

- Converts the PS/2 port on the KVM Switch to USB KVM Device (PC, Mac or SUN Platforms)

- Supports Standard PS/2 mouse and Microsoft IntelliMouse

- Supports Data Transfer Rate up to 12Mbps Speed

- Supports BUS-Power, no External Power Adapter Required

- Supports Plug & Play and Easy Installation

- 2-Year Warranty

Specifications					Solution for TU-PS2

| Hardware |
| --- |
| Interface | USB 1.1, 1.0 Interface Type A and PS/2 |
| Standards | PS/2 Keyboard & Mouse |
| OS Compliant | Windows 98SE/ME/2000/XP Netware 4.11, 5.0 HP Unix, Linux. Mac G3/G4, OS 8.6 or above Sun Microsystems |
| Cable Length | 3.5cm (1.37 inches) |
| Cable Gauge | 28/24 AWG |
| Data Rate | 1.5Mbps |
| Power Consumption | 500mA (max) |
| Weight | 51g. (0.1 lb) |
| Operating Temperature | 5( ~ 40( C (41( ~ 104( F) |
| Storage Temperature | -20( ~ 60( C (-4( ~ 140( F) |
| Humidity | 0 ~ 85% (Non-Condensing) |
| Certification | FCC, CE |

Package Contents			System Requirement

- TU-PS2				-    System with Supported Operating System

-     Quick Installation Guide		-    Available USB 1.1 Compliant Port

# Text boxes

TU-PS2

USB to PS/2 Converter

This USB to PS/2 converter allows you to connect a PS/2 keyboard and mouse to a USB port on your Desktop or Laptop PC.

TU-PS2 (v1.1R)