Features

- Wi-Fi Compliant with IEEE 802.11b/g Devices on 2.4 GHz ISM Frequency Band

- Wireless Supports Infrastructure and Ad-Hoc Modes

- Wireless Supports WEP 64/128-Bit Encryption (ASCII & HEX)

- Supports High Quality MPEG4 Compression

- Supports Day and Night Vision with IR Lens

- Supports Audio Monitoring and RS-485 Port for PAN & TILT Control

- Supports CCD Image Sensor and DC-Iris Control

- Supports DirectX 9.0 Control for Internet Explorer

- Allows for Remote Access from Web Browser for Live Image Viewing

- Supports TCP/IP networking, SMTP e-mail, HTTP and other Internet related protocols

- Supports Web configuration with password protection

- Powerful Windows IPView SP Application Software for multiple cameras monitoring, image capturing, and video recording (Windows 98/ME/2000/XP)

- Built-in I/O Ports to Trigger Alarm and Email Notification

- Broad Range of Applications for Monitoring Homes, Offices, Banks, Hospitals, and a Variety of Private and Public Monitoring

- 3-Year Warranty

Specifications

| Camera Specifications | Hardware Specifications |
| --- | --- |
| Image Sensor | System |
| Sensor | Sharp 1/4” type CCD IR on: 0 lux ; IR off: 1 lux | CPU | Philips Trimedia PNX1300 VLIW DSP |
| Resolution | 512 x 480(NTSC), 512 x 576(PAL) | RAM/Flash ROM | 16Mbytes/2Mbytes |
| Lens | Built-in f 6.0mm F1.8 IR Lens (CS-Mount Standard, Replaceable) | OS | Linux |
| Audio | I/O & Control |
| MIC Input | Internal MIC (mono) S/N ratio: More than 60dB Frequency: 50 ~ 16000Hz | Generic Input | 1 set, 2 pin (photo coupler, 12V DC 50mA max) |
| Speed | 24Kbps bit Rate 8K Sampling Rate | Generic Output | 1 set, 2 pin (relay, 24V DC 1A/125V AC 0.5A) |
| Video | RS-485 | 2 pin (Half Duplex) |
| Frame Rate | 30fps@CIF(NTSC), 25fps@CIF(PAL) | Requirements |
|  |  | Memory Size | 128M (256 Recommended) |
| Compression | MPEG4 short header mode compression | Pentium III, 450 MHz or above VGA card resolution: 800 x 600 or above |
| Resolution | CIF(350x240NTSC, 352x288PAL) QCIF(176x120NTSC, 176x144PAL) | Physical/Environmental |
|  |  | Dimension | 195x90x50 mm (7.7x3.5x2 inches) |
| Up/Down Reversal | Yes | Weight | 270 grams (9.5 oz) |
| Left/Right Reversal | Yes | Stand Height | 120 mm (4.7 inches) |
| Bit Rate Selection | 8 Levels | Power | 12V DC, 1.5A External Adapter |
| Quality Selection | 5 Levels | Consumption | 7 watt ( 580mA x 12V), max |
| Max Frame Rate Selection | 9 Levels | Temperature | Operating: 5(C ~ 40(C (41(F ~ 104(F) Storage: -25(C ~ 50(C (-13(F ~ 122(F) |
| Control | Yes (Brightness/ Contrast/ Flicker/ Saturation/ Hue) | LED | Power: Blue Link/Active: Red |
| Motion Detection | Yes |  |  |
| Gain/Exposure/White Balanced Control | Automatic | Humidity | 5% ~ 95% Non-Condensing |
|  |  | Certifications | FCC. CE, VCCI Class B |
| Iris Level | Adjustable VR for Iris Control Adjustment | Communication |
|  |  | LAN | 10/100Mbps Ethernet, Auto-Sensing |
| Wireless |  |  |
| Standard | IEEE 802.11b/g | Protocol | HTTP, SMTP, FTP, Telnet, NTP, DNS, DHCP, TCP/IP, DDNS, UPnP |
| Data Rate | 11g: 54, 48, 36, 24, 12, 9 & 6Mbps 11b: 11, 5.5, 2 & 1Mbps |  |  |
| Module Technique | DSSS | Software |
| Frequency | 2.4 ~ 2.4835Ghz (ISMB) | Browser | IE 5.0 or above |
| Antenna | Detachable 2dBi Diversity Antenna (Reversed SMA Connector) | Application | IPView SP Software |
|  |  | OS Support | Windows 98SE, ME, NT4, 2000,XP |

* NTSC: US Version ; PAL: AU/EU/UK Version

To order please call: 888-326-6061

3135 Kashiwa Street • Torrance, CA 90505 • (310) 891-1100 • Fax: (310) 891-1111

Sales: sales@trendware.com • Support: techsupport@trendware.com

Tech Support Hotline: (310)626-6252

www.TRENDNET.com

# Text boxes

Advanced Wireless Day/Night

Internet Camera Server

TRENDnet's TV-IP300W Internet Camera Server is the perfect device for remote monitoring and transmitting real-time events over the Internet. The TV-IP300W functions as a video/audio/surveillance camera allowing you to view live events with your web browser via Internet or Intranet. Up to 4 cameras can be remotely managed with the bundled IPViewSP software. This Internet Camera Server has MPEG4 quality streaming video, automatic image capture, and event notification via e-mail, making it the ideal solution for Internet video broadcasting applications.

TV- IP300W

Network Solution for TV-IP300W