Features

- Wi-Fi Compliant with IEEE 802.11b/g Devices on 2.4 GHz ISM Frequency Band

- Wireless Supports Infrastructure and Ad-Hoc Modes

- Wireless Supports WEP 64/128-bit Encryption (ASCII & HEX)

- Built-in Pan & Tilt Control for More Flexible Monitoring

- Supports 4x Digital Zoom for Close Up Images

- Supports Both Active X control for Internet Explorer and Java applet for IE and Netscape Navigator

- Allows for Remote Access from Web Browser for Live Image Viewing

- Supports TCP/IP networking, SMTP e-mail, HTTP and other Internet related protocols

- Supports in a mixed Operating System Environment such as Windows and Macintosh

- Supports Web Configuration with Password Protection

- Powerful Windows IPView Application Software for multiple cameras monitoring, image capturing, and video recording (Windows 98/ME/2000/XP)

- Broad Range of Applications for Monitoring Homes, Offices, Banks, Hospitals, and a Variety of Private and Public Monitoring

- 3-Year Warranty

Specifications

| Camera | Hardware |
| --- | --- |
| Image Sensor | System |
| Sensor type | 1/4” Color CMOS Sensor | CPU | RDC R2880 |
| Resolution | 640 x 480 | RAM/Flash | 8Mbytes/2Mbytes |
| Fixed Lens | Built-in f: 6.0mm F: 1.8 | OS | RTOS |
| Min. Illumination | 2.5lux@f1.4,3000K color |  |  |
| Communication | Pan & Tilt |
| LAN | 10/100Mbps Ethernet, Auto-Sensing | Pan | -156( ~ +156( |
| Protocol | HTTP, FTP, TCP/IP, UDP, ARP, ICMP, BOOTP, RARP, DHCP, PPPoE, DDNS, UPnP | Tilt | -45( ~+70( |
| Video / Image | Control | Up, Down, Right, Left, Center |
| Frame Rate | 30fps@QCIF 25fps@CIF 10fps@VGA | Requirements |
|  |  | Memory Size | 128M (256 Recommended) |
| Compression / Selection | JPEG / Yes | Pentium III, 450 MHz or above VGA card resolution: 800 x 600 or above |
| Resolution / Frame Rate Setting | 160 x 120, 320 x 240, 640 x 480 / 1, 5, 7, 15, 20, auto | Physical/Environmental |
|  |  | Dimension | 117x115x105 mm (4.6”x4.5”x4”) |
| Left/Right Reversal | Yes | Weight | 0.3kg (0.75lb) |
| Up/Down Reversal | Yes | Consumption | 8 watt ( 1600mA x 5V), max |
| Gain/Exposure/White Balanced Control | Automatic | Power | 5V DC, 2.5A External Adapter |
| Digital Zoom | 4x | Humidity | 5% ~ 95% Non-Condensing |
| Compression Rate | 5 Levels | Temperature | Operating: 5(C ~ 40(C (41(F ~ 104(F) Storage: -25(C ~ 50(C (-13(F ~ 122(F) |
| Light Frequency | 50Hz / 60Hz |  |  |
| Wireless | LED | Power: Green Link/Active: Orange |
| Standard | IEEE 802.11b/g |  |  |
| Data Rate | 11g: 54, 48, 36, 24, 12, 9 & 6Mbps 11b: 11, 5.5, 2 & 1Mbps | Emissions | FCC. CE |
| Module Technique | DSSS | Software |
| Frequency | 2.4 ~ 2.4835Ghz (ISMB) | Browser | Internet Explorer (5.0 or above) or Netscape Navigator (6.0 or above) |
| Antenna | Detachable 2dBi Diversity Antenna (Reverse SMA Connector) | Application | IPView Software |
| Encryption | Disable/64/128-bit WEP, WPA-PSK | OS Support | Windows 98SE, ME, NT4, 2000,XP |

Package Contents				Related Products

- TV-IP400W					- TV-IP100/100W

- Multi-Language QIG				- TV-IP200/200W

- CD-ROM (Utility& User’s Guide)		- TV-IP300/300W

- Power Adapter (5V DC, 2.5A)			- TV-IP400

- RJ-45 Cable (1.5m)

- Mounting Frame

To order please call: 888-326-6061

3135 Kashiwa Street • Torrance, CA 90505 • (310) 891-1100 • Fax: (310) 891-1111

Sales: sales@trendnet.com • Support: techsupport@trendnet.com

Tech Support Hotline: (888)777-1550

www.trendnet.com

# Text boxes

Advanced Pan & Tilt Wireless Internet Camera Server

The Pan/Tilt IP Camera is a full-featured surveillance system that provides high quality video over a wireless network connection.  Built-in CPU and Web Server allow the camera to function as a standalone device, allowing users to access the camera anywhere in the world by using a Web browser.  Users can also move the camera remotely in almost any direction, scanning sensitive locations for unauthorized intrusion.  The IP Camera comes with a CMOS sensor to deliver clear and crisp images, and its powerful IPView software gives users enhanced security options to archive streaming video straight to a computer’s hard drive.  IP View software can also monitor multiple cameras on a single screen, enable motion detection to trigger automatic recording, and send email alert notification.

Network Solution for TV-IP400W

TV- IP400W