Features

- Supports up to 4 channels of real-time concurrent voice and / or fax communications.

- Field programmable CP tone detection and generation to support PBX and CO line interconnections.

- Supports programmable line interfaces with country specific telephone settings.

- Supports ITU standard voice codecs and voice processing algorithms including G.711, G.723.1, and G.729 A/B, and G.168 Echo Cancellation as well as Fax T.30 and T.38

- Intuitive management interfaces (Web, Telnet and Console) ensures rapid deployment / reduces demands on MIS resources.

- Network administrators can remotely monitor and perform routine maintenance / trouble-shooting via Internet browser or telnet session.

- H.323 standard v.3 compliant (including H.323 fast-start mode) ensure interoperability with 3rd Party H.323 Standards Compliant Devices.

- Supports IP Precedence prioritized Voice before Data packets providing best effort QoS

- Built-in TFTP and Flash memory for firmware download and upgrade via network

- Support Call forwarding and Call Transfer

- Supports Dynamic IP/ PPPoE client support

- Supports DHCP client support

- Supports Dynamic DNS for deployed in a dynamic IP environment

- Bulk Call successful rate over 99.98%

- Recommend to use with dedicated broadband connection

- 5-Year Warranty

Technical Specifications

| Telephony Interface |
| --- |
| Physical interface | Desktop with 4 Analog Ports • Loop start 2 x FXO (RJ-11) • Loop start 2 x FXS (RJ-11) |
| Programmable line interfaces | Complex line impedance |
| Protocols | H.323v3 (Normal/fast-start mode) Supports gateway-gateway direct routing and gateway-gatekeeper assisted routing mode |
| Voice coders support | ITU-T G.711 u-law, G.723.1, and G.729A/B, auto-switching (Frame-rate/packet: 1 – 8) |
| Fax | Supports T.30 G3 fax on PSTN Interface; ITU-T T.30 fax spoofing; ITU-T T.38 |
| Simultaneous connections | 4 channels voice/fax |
| Media processing | Gain control; G.168 echo cancellation (16 ms); Voice activity detection (VAD); Comfort noise generation (CNG); Call progress detection; DTMF detection/filtering/regeneration (H.323v3/IMTCv1) |
| Data Network Interface |
| Physical interface | LAN: 1 (10Base-T/100Base-TX, Auto-Negotiation) |
| Protocols | TCP/IP, DHCP, HTTP, DNS |
| Advanced functions | IP Precedence, PLAR, DDNS |

| System |
| --- |
| Call Control | Built-in three-tier dialing plan and destination hunting Supports gatekeeper authorization and accounting Supports gatekeeper call routing control and gateway mapping Call accounting information on gateway (via RS-232) or gatekeeper |
| Management | RS-232 (DCE mode) Built-in HTTP Web-based remote management Telnet remote management |
| System upgrade | Flash memory and built-in TFTP allowing firmware and feature upgrade via network |
| LED Indicators | System: 2 Power, CPU LAN: 4, Link/ACT, Speed, Collision Voice: 2 per channel (Ringing, Active) |
| Interoperability | Microsoft NetMeeting*; Cisco AS5300, 3600; RADVISION gatekeeper; Cisco gatekeeper |
| Dimensions (L X W X H) | 241 x 135 x 45 mm (9.5 x 4.3 x 1.8 inches) |
| Weight | 1.9 kg (4.2 lb) |
| Input Voltage, AC | 90-260 VAC, auto ranging, 50-60 Hz |
| Power | 12V DC, 2A (External Power Adapter) |
| Operating environment | Operating temperature: 0° ~ 50° C (32° ~ 122° F) Humidify: 90% (non-condensing) |
| Certifications | CE; FCC, UL |

Telephony Line Module Specifications

| FXO Ports |
| --- |
| Signaling | Loop start/DTMF |
| Number of channels | 2 |
| Interface connectors | 2 RJ-11 2-pin modular jacks |
| Line impedance | 600900 Complex line impedance |
| Insertion loss | 2 dB nominal |
| Frequency response | 300 Hz ~ 3400 Hz +/- 2 dB w.r.t. 1004 Hz |
| Return loss | 18 dB |
| Input level adjustment | -6 dB to +6 dB |
| Output attenuation | 0 dB to 13 dB |
| Longitudinal balance | 45 dB |
| Disconnect detection | Loop current; Customizable tone detection |
| FXS Ports |
| Signaling | Loop start/DTMF |
| Number of channels | 2 |
| Interface connectors | 2 RJ-11 2-pin modular jacks |
| Line impedance | 600900 Complex line impedance |
| Insertion loss | 2 dB nominal |
| Frequency response | 300 Hz ~ 3400 Hz +/- 2 dB w.r.t. 1004 Hz |
| Return loss | 18 dB |
| Input level adjustment | -6 dB to +6 dB |
| Output attenuation | 0 dB to 13 dB |
| Longitudinal balance |  45 dB |
| Loop current | 25 mA nominal |
| Ring voltage | 40 Vrms nominal |
| Ringing tone | 16.67 Hz, 20 Hz (default), 25 Hz or 50 Hz |
| Disconnect detection | Loop current |

### REASONS WHY IS THE TVP-221H IS THE LASTING TREND

| Easy Implementation | Intuitive, user-friendly, yet powerful management interface (Web / Telnet / console), that can dramatically reduce IT personnel resource requirements, and complete VoIP deployment in a short time. |
| --- | --- |
| Cost Reducing | Eliminate cost of long distance calls and pay for local calls only. |
| Traffic Control | Integrate Voice and Data and Controls network traffic with QoS, DMZ, and Virtual Server. |

VoIP Application Diagram

Packaging Contents				Related Products

- TVP-221H					- TVP-224HR

- Quick Installation Guide

- CD-ROM (User’s Guide)

- Cat 5 Cable (1.8m/6ft.)

- RS-232 Cable

- Power Adapter (12V DC, 2A)

To order please call: 888-326-6061

3135 Kashiwa Street • Torrance, CA 90505 • (310) 891-1100 • Fax: (310) 891-1111

Sales: sales@trendware.com • Support: techsupport@trendware.com

www.TRENDnet.com

# Text boxes

4-Port VoIP Gateway

The TRENDWARE TVP-221H is a Voice over IP (VoIP) gateway providing Toll Class voice quality and manageability from an intuitive yet powerful user interface. The TVP-221H VoIP Gateway is an H.323 Standards Compliant Gateway with 4 analog telephony ports (2 FXS and 2 FXO) allowing for up to 4 concurrent voice connections. This combination of analog telephony ports gives users the flexibility of making direct VoIP calls via analog phone/fax device or through PBX/CO lines respectively.

TVP-221H