## FEATURES

- Built-in 4-port 10/100Mbps Auto-Sensing Switch

- Supports Cable Modem/xDSL Modem (Dynamic/Static IP, PPPoE, PPTP) and FTTH (Fiber to

the Home) connections

- Supports most operating systems, such as Windows 95/98/ME/NT/2000/XP, Unix, and Mac

- Website Access Restriction using URL Keywords and Services Types

- Supports DMZ and 40 Virtual Servers(Port Forwarding)

- Supports Static Routing and Dynamic DNS Service

- Supports 100 sessions of VPN Pass-Through for PPTP, IPSec and L2TP (when each VPN

client connects to a different VPN endpoint)

- Supports UPnP (Universal Plug & Play)

- ALGs (Application Level Gateways) and Special Application support for programs which are

difficult to use behind a Firewall

- NAT (Network Address Port Translation) /NAPT Support

- Firewall features includes Stateful Packet Inspection (SPI) protects against DoS attacks

- Real-Time e-mail alert and logs when attack/unauthorized Internet activity occurs

- Easy Configuration using Web Browser

- DHCP Server supports up to 253 clients

- Remote Management with HTTP/Web Browser (from LAN, WAN, or both)

- Flash memory for firmware upgrade and save/restore router configuration

- 5-Year Warranty

## TREND SPEC’S

Standards:	IEEE 802.3, 802.3u

Protocols:	NAT, PPPoE, HTTP, DHCP, TCP/IP, UDP, PAP, CHAP, RIP1, DDNS

Firewall:	NAT firewall, Attack Alert (email) and log, Stateful Packet Inspection firewall for DoS (Denial of Service) attacks

Security:	URL Filter, Access Control, Local Password

Local Port:	4x 10/100Mbps Ethernet port (RJ45), Auto-MDIX

Internet Port:	1x 10/100Mbps Ethernet port (RJ45)

LEDs:	Power, Status, Lnk/Act and 100 (LAN 1~4), WAN

Power:	9V DC 600mA External Power Adapter

Dimensions (LxWxH):	141 x 100 x 27 mm (5.5x 3.9 x 1.06 inches)

Weight:	Appr. 363g  (12.8 oz.)

Temperature:	Operating:  0˚ to 40˚ C (32˚ to 104˚ F)

Storage: -10˚ to 70˚ C (14˚ to 158˚ F)

Humidity:	Operating: 0 % ~ 80 % (non-condensing)

Storage: 0% ~ 95% (non-condensing)

Certifications:	FCC, CE, VCCI

### TOP REASONS THE TW100-BRF114 IS A LASTING TREND

Easy Integration: With the built-in 4-port 10/100Mbps Switch, you can integrate this device to any Ethernet/Fast Ethernet Network.

Cost-Effectiveness: Share the broadband Internet connection, saves router costs and account charges.

Security: Firewall protection keeps hackers out.

Performance: Experience the high speed Internet access while reducing network traffic.

Product Information

TW100-BRF114	Cable/DSL 4-port Firewall Router

TW100-BRV204	Cable/DSL VPN Firewall Router

TW100-BRV304	Cable/DSL Advanced VPN Firewall Router

TW100-S4W1CA	10/100Mbps DSL/Cable Broadband Router /w 4-port Switch

To order please call: 888-326-6061

3135 Kashiwa Street • Torrance, CA 90505 • (310) 891-1100 • Fax: (310) 891-1111

Sales: sales@trendware.com • Support: techsupport@trendware.com

www.TRENDNET.com

# Text boxes

TW100-BRF114

Cable/DSL 4-Port Firewall Router

TRENDnet's TW100-BRF114 4-Port Cable/DSL Firewall Router allows multiple users to share internet access protected from unwanted intruders via a robust Stateful Packet Inspection Firewall (SPI). The Firewall provides advanced protection against popular Denial of Service attacks. Multiple Web Patrol features allow parents and Network Administrators to restrict internet access based on clients' IP Addresses, Time/Date, URL Keywords, and Service Types. Setting up the router is effortless with the Web Browser Configuration. Surf and share the Internet with ease knowing that your computers and information are safely protected!

Network Solution for TW100-BRF114